## Slide 1: Introduction to Image analysis
Robert Haase, HongKee Moon, Benoit Lombardot
MPI-CBG, Scientific Computing Facility
October 23rd – 25th 2017
1. Introduction & Basic concepts
Section goals :
Introduction to the course, image analysis and Fiji
Image characteristics and visualization
Regions of interest and measures

## Slide 2
Ian Henry: Facility Leader
BSc: Molecular Biology (Edinburgh)
PhD: Genetics/Bioinformatics (Nottingham)
Image Processing
Benoit Lombardot
Senior Image Analyst
MSc: Cognitive Science (Paris)
PhD: Bioimage analysis (Paris)
Bioinformatics
Holger Brandl:
Senior Data Engineer
Diploma: Biomathematics (Greifswald)
PhD: Computer Science (Bielefeld)
Naha Lakshmanaperumal
Bioinformatician
BSc: Biotechnology (Tamil Nadu)
MSc: Bioinformatics (Saarland)
Scientific Software
Development
Peter Steinbach
HPC Developer
Diploma: Physics (Leipzig)
PhD: Particle Physics (Dresden)
HongKee Moon
Software Developer
B.Eng: Computer Science (Seoul)
M.Eng: Computer Science (Seoul)
“The Scientific Computing Facility aims to provide a unified service to assist researchers in the tackling of scientific questions involving computational analysis, large data handling and image processing.”
Robert Haase
Image Analyst
Diploma: Computer Science (Dresden)
PhD: Medical Radiation Sciences (TUD)
Image Analysis, Intro & basic concepts
Scientific Computing Facility (SCF)
Notes: Bio Image informatics service is embedded in the SCF:
Together with bioInformatics and Scientific software development

## Slide 3: Overview
Day 1:
Introduction & basic concepts
Segmentation 1
Day 2:
Measure in time sequence and tracking
Segmentation 2
Day 3:
Visualize and Explore 3D images
Spot detection and segmentation in 3D
Image Analysis, Intro & basic concepts
Notes: Blocks a 6/7 slides presenting concepts and tools followed by guided exercises
Blocks start with basic ideas and gradually introduce more complex things
For the exercise we try to have a template that you can follow
The course is an introduction assuming you never have open Fiji (ask a few question to get the room level)
We’ll walk in the room to help
Use Stickers (Green=done!, Red=Help me! ) it will help us adjust timing
For part 5 and 6 At the end the course you’ll exercise/demo you like
1 or 2 depending on time

## Slide 4
Image Analysis, Intro & basic concepts
Image analysis (1/2)
This is not
Image Analysis

## Slide 5
Image Analysis, Intro & basic concepts
Image analysis (2/2)
Notes: There a few people on the campus working on Image analysis service (IAS). I worked in an IAS
With that presentation we would like to give you a flavour of what IA can do for you and how we can help
Probably all familiar with photoediting software. Make a picture cuter! A subjective process
Doing IA for science is different needs objectivity which imply quantification, repeatability
I you have image and good question, there are a lot of soft that can help you.
And if you go in this rigorous way and work maybe in a few years you can win a medal
Transition: However in practice IA is not just one more step in your research pipeline

## Slide 6: Image Analysis, Intro & basic concepts Bio Image Analysis
Image preparation:
Deconvolution
Image fusion
Sequence alignement
Bleaching correction
Bleed through correction
…

## Slide 7: Image Analysis, Intro & basic concepts Bio Image Analysis
Image preparation
Object definition Segmentation:
Identification of points, lines, surfaces, volume of interest
Standard pipeline and toolbox: filters, threshold, mathematical morphology, watershed, maxima detection, …

## Slide 8: Image Analysis, Intro & basic concepts Bio Image Analysis
Image preparation
Object definition Segmentation
Characterization:
Objects characteristics measures
Inter object relation
Modelling
Significance test

## Slide 9: Image Analysis, Intro & basic concepts Bio Image Analysis
Image preparation
Object definition Segmentation
Characterization
Interaction, Visualisation, Automation:
Input data
Explore data
Curate segmentation
Script analysis pipeline

## Slide 10: Image Analysis, Intro & basic concepts Bio Image Analysis
Image preparation
Object definition Segmentation
Characterization
Interaction, Visualisation, Automation

## Slide 11
Amira
Huygens
Knime
Cell profiler
Volocity
Illastik
Imaris
Arivis
Matlab
Free/Commercial,
Customize versus ease of use
Specific pipelines: slide analysis, HCS, neurons, 3D visualization,
large dataset
Python
Fiji
Image Analysis, Intro & basic concepts
Image analysis software
Notes: Word-clouds: ease of use vs. customization
pro vs. cons
typology and location on campus (present each other, who are the people that provide the service?)

## Slide 12
Image Characteristics
and Visualization
Notes: Blocks a 6/7 slides presenting concepts and tools followed by guided exercises
Blocks start with basic ideas and gradually introduce more complex things
For the exercise we try to have a template that you can follow
The course is an introduction assuming you never have open Fiji (ask a few question to get the room level)
We’ll walk in the room to help
Use Stickers (Green=done!, Red=Help me! ) it will help us adjust timing
For part 5 and 6 At the end the course you’ll exercise/demo you like
1 or 2 depending on time

## Slide 13: Open images
Image Analysis, Intro & basic concepts

## Slide 14: Stitching
Image Analysis, Intro & basic concepts
Image source: Carine Stapel (Vastenhouw lab)

## Slide 15: Stitching
Image Analysis, Intro & basic concepts
To do any analysis we need to create a single image
 Stitching (Menu Plugins > Stitching > Grid/Collection stitching)
Image source: Carine Stapel (Vastenhouw lab)

## Slide 16: The image interface
Image Analysis, Intro & basic concepts
Dataset positions
Zoom factor
Image type
Image size in physical units (and in pixels)

## Slide 17
Image Analysis, Intro & basic concepts
Graylevel image
0
255
Notes: A Gray Level image,
Color image is a superposition of 3 gray level images (Red, Blue, Green)
Multi channel image superimpose multiple images with various colors (this is often the image acquired on microscopes)
In fluorescence microscopy each channel represent different view (the spatial organisation of a protein for instance).
We usually analyze the channel 1 by one 1,
also most of the tools are meant for graylevel image

## Slide 18
Image>Lookup Tables
Image>Colors>Display LUTs
Image Analysis, Intro & basic concepts
Look Up Tables (LUT)
Notes: Also try Image>Colors>Display Luts

## Slide 19
Image Analysis, Intro & basic concepts
Bit depth
Pixel value range
Sensitivity of your camera (8, 12, 16 bits)
The more bits the more possible values
?
Notes: Depends on your camera sensitivity.
Camera can acquire more different intensity than the eye or a screen can actually perceive at the same time.
However using the level control one can see any sub part of the intensity scale.
It is also possible to “compress” the scale to see everything at once (but then the intensity you see are modified)
Regarding the question mark: looking at the image can’t allow to answer (eye, display limitation)
8-bit : 0 to 255 (28-1)
16-bit: 0 to 65535 (216-1)
Remark: a particular image might not use all the range

## Slide 20: Pixel/Sampling size
Image Analysis, Intro & basic concepts
Menu Image > Properties
Pixel size: 3.3 µm
Pixel size: 0.8 µm
Pixel size: 0.2 µm
Pixel size: 0.05 µm
Pixel size is the distance between 2 measure points
Notes: Pixel size will have an impact on your area measure

## Slide 21: Resolution
“The measure of how closely lines can be resolved in an image is called spatial resolution”
  Source: https://en.wikipedia.org/wiki/Image_resolution
Image Analysis, Intro & basic concepts
Notes: Pixel size and resolution are not the same thing
2 image with same pixel size but different resolution

## Slide 22: Histogram
Image Analysis, Intro & basic concepts
Intensity
Number of pixels
Background
Objects
Number of pixels
Intensity
Background?
Object?
Notes: The frequency/occurence of each intensity value.
A summary of the image.
Convenient for the computer which only sees a list of numbers
And does not perceive the spatial organisation in the image like us

## Slide 23: Histogram
Image Analysis, Intro & basic concepts
Notes: The frequency/occurence of each intensity value.
A summary of the image.
Convenient for the computer which only sees a list of numbers
And does not perceive the spatial organisation in the image like us

## Slide 24: Visualization: Brightness/Contrast
Define the grey value range to visualize
Also known as “windowing”
Menu Image > Adjust > Brightess/Contrast or SHIFT+CMD+C
Image Analysis, Intro & basic concepts
0
255

## Slide 25: Visualization: Brightness/Contrast
Define the grey value range to visualize
Also known as “windowing”
Menu Image > Adjust > Brightess/Contrast or SHIFT+CMD+C
0
255
85
Image Analysis, Intro & basic concepts

## Slide 26: Visualization: Brightness/Contrast
Define the grey value range to visualize
Also known as “windowing”
Menu Image > Adjust > Brightess/Contrast or SHIFT+CMD+C
0
255
85
48
Image Analysis, Intro & basic concepts

## Slide 27
Image
  Pixels = measure points
    Measure = pixel value
    Sampling distance = pixel size
  Bit depth indicate the possible pixel value
  The histogram gives a summary of value in a given image
Visualisation
  Visualization does not modify data
  It adapts image to our perception
  Look Up Table : each value can be associated to a color
  Brightness and contrast allow to change the visualized range
Image Analysis, Intro & basic concepts
Gray level image summary
Notes: The screen can’t display, your eyes can’t perceive all the grey level at once
If you believe only what you see you loose information (similar as when you saturate your acquisition sensor)

## Slide 28
Demo
Notes: Load an image (blobs)
Show the viewer, zoom and pan option
Properties
The command finder
Load (Hella cells)
Show the channel tool and visualization mode
Show pixel value with the mouse
Define pixel size, add a Scale
Show the luts
Show the lut overlay
Show brightness and contrast
Show a 16 bit image (M51 galaxy)
Reproduce mri stack visualisations
Show a color image and a composite image (clown.jpg, hella cells)
To RGB stack, channel control,
Split and merge to go back to a
Can do the stitching hands on if we are in advance (folder to_stitch, snake organisation , x*y = 5*2)

## Slide 29
Image Analysis, Intro & basic concepts
Command finder
Press the “L” key
Notes: Any color can be choosen for the channel
Functionnal meaning of the protein

## Slide 30
Image Analysis, Intro & basic concepts
Color Images
Additive color synthesis
Red Green Blue decomposition
Notes: http://en.wikipedia.org/wiki/RGB_color_model credit for the image
Take that value of your image can be change

## Slide 31
Image>Type>RGB Stack  red, green and blue image stack.
Image>Color>Channel Tool
Image Analysis, Intro & basic concepts
Color Images decomposition
Notes: Check the properties of the image 1 channel to 3 channel

## Slide 32
Channels can be visualized simultaneously
Image>Color>Channel Tool>Composite
Image Analysis, Intro & basic concepts
Composite Images
Notes: Any color can be choosen for the channel
Functionnal meaning of the protein

## Slide 33
Image Analysis, Intro & basic concepts
Image summary
d
Pixel Size
Pixel value, Bit depth
Gray level image
Histogram
Visualisation
B&C
LUTs
RGB , Composite Images
Combine gray level images
Notes: The screen can’t display, your eyes can’t perceive all the grey level at once
If you believe only what you see you loose information (similar as when you saturate your acquisition sensor)

## Slide 34
Exercises
Notes: More time for exercise than previous years
Not all the specific tools you need have been demonstrated
Ask the command finder, each other, google
what tool and how to use it ?
If you are through:
Help you neighbors!
ask us what is next!

## Slide 35: Histogram
To which of the three images/ROIs does this histogram belong to?
Image Analysis, Intro & basic concepts
For each image, try interpret its histogram and comment its appearance with your neighbors.
Notes: 1- how to show an histogram

## Slide 36: Exercise
Image Analysis, Intro & basic concepts
Prepare image for presentation
  Open the image cell_layer2.tif
  Split channels
  Merge channel 1 and 3
  Update channel 1 lut to magenta
  Adapt contrast of each channel
  Convert type to RGB
  Add a scale bar
  Save as Tiff
  Try to load in a ppt/keynote

## Slide 37
Manual Measurements

## Slide 38: Image Analysis, Intro & basic concepts Measure workflow
Select a tool and Draw a ROI
Analyze>Set measurements
Analyze>Measure (press M key)
 Creates a result table
Results>File>SaveAs
Export data for analysis
Open an Image
Notes: Whenever a tool selection is visible it will influence measure
If no selection is there the measure is made on the whole image

## Slide 39: Image Analysis, Intro & basic concepts The Regions of Interest (ROIs)
Region tools:
Rectangle, rounded rectangle
Oval, orientable ellipse, brush tool
Polygon, free form, Wand tool
Line tools : Straight, segmented, free
Point tools : Point, Multi-Point
Interactively Edit ROIs
Double click to see the option
Notes: Presentation of menu content

## Slide 40: The Regions of Interest (ROIs)
There are more tools in the toolbar than expected…
Image Analysis, Intro & basic concepts
Use right-click and double-click to uncover them

## Slide 41: The Regions of Interest (ROIs)
Image Analysis, Intro & basic concepts
draw a rectangle
using the rectangle tool
Hold SHIFT to unite objects
draw a circle
using the circle tool
add objects to the ROI
by holding SHIFT
unite objects to the ROI
by holding SHIFT
subtract objects to the
ROI by holding ALT
move the ROI
by clicking inside and move the mouse
delete the ROI
by clicking outside
Recover the last ROI
by using menu Edit > Selection > Restore Selection (SHIFT+CMD+E)

## Slide 42: Image Analysis, Intro & basic concepts ROIs & Measures
For measurements details : http://rsb.info.nih.gov/ij/docs/menus/analyze.html#set
Analyze>Set Measurements…
Then press “M” or menu
Analyze>Measure
Notes: Presentation of menu content

## Slide 43: The ROI Manager
Menu Analyze > Tools > ROI Manager…
Image Analysis, Intro & basic concepts
Notes: store ROIs
Compare, Combine, Edit ROIs
Measure one ROI on multiple images
Measure multiple ROI simultaneously
Prepare ROI before sending them to the overlay

## Slide 44: ROI Manager & Measures
Visualize, label and measure ROIs
Image Analysis, Intro & basic concepts
Notes: Save roi, save measure.
Color roi to make them more informative.
Transition:
Only one roi at a time what does show all does? It sends roi to the overlay

## Slide 45: Image Analysis, Intro & basic concepts Image overlay
Menu Image>Overlay>Add selection
Interest:
Visualisation purpose
Image from : http://blogs.qub.ac.uk/ccbg/files/2014/05/2014-05_Analyzing_fluorescence_microscopy_images.pdf

## Slide 46: Image Analysis, Intro & basic concepts Summary
Mesure pipeline
Storing regions
Roi manager
Overlay

## Slide 47
Demo
Notes: Open an image (fluorescentCells.tiff)
Count nuclei
Create rois of nuclei
Measure nuclei intensity and area
The exact shape does not matter for the average intensity
Measure another marker intensity inside the nuclei
Interpretation of the intensity measure
Interpretation of the area (pixel size)
Save the image with overlay and reopen it
Save flatenned image and show

## Slide 48: Exercise
Image Analysis, Intro & basic concepts
Measure embryo average size
  Open Embryos.jpg
  Use roi to measure embryos diameter.
  Save the result table
  Open it in excel and measure the average radius
  Add an overlay to the image and save it
  Flatten image and save it too
  Open image in ppt
  Meaning of the intensity?
Notes: Can do the stitching hands on if some time is left