## Slide 1: Introduction to Image Analysis
Robert Haase, Benoit Lombardot
Measurements in time sequences & tracking
Contents
Image correction
Visualisation
Measurements in time sequences
Tracking

## Slide 2: Quiz
Given that image and the corresponding histogram:
Which threshold would you choose to differentiate black objects from the from the white background?
12
123
234

## Slide 3: Quiz
I was just drawing this red line along my scale bar.
What’s the images pixel size?
0.5 µm
0.01 µm
0.05 µm

## Slide 4: Quiz
If I measure the signal in the white ROI, what will be my measurement if I press the M key?
Signal in the green channel
Signal in the red channel
Signal in the blue channel

## Slide 5: Quiz
What operation do we need to apply to get this result?
?

## Slide 6: Quiz
What could be done to improve the threshold result?
Thresholding
X + Thresholding
Draw a ROI
Subtract background
Gaussian blur

## Slide 7: Overview
Image correction
  Image registration
  Motion correction
  Bleaching correction
Visualisation
  Kymography
    How to build kymographs
    How to interpret kymographs
  Visualisation of time sequences in Imaris (Demo)
Tracking
  Introduction / Theory
  Single particle tracking
  Trackmate demo
  Exercise
Measurements in time sequences

## Slide 8: Definition: Registration
Measurements in time sequences
x
y
x
y
Technically, that means finding corresponding structures and
determining the optimal transformation to correct the misalignment of the images and apply the transformation.
x
y
“Image registration is the process of transforming different sets of data into one coordinate system.”
Source: Wikipedia

## Slide 9: Terminology: Naming images
Most commonly, one image is moved/rotated/… to match it in the coordinate system of the other image.
Measurements in time sequences
x
y
Reference,
source or
fixed image
Target,
subject or
moving image

## Slide 10: Registration strategies
Feature-based
Measurements in time sequences
versus
Intensity-based
Mean squared error of pixel values
MSE = 2000
MSE = 0
MSE = 1900
MSE = 500
System of linear equations
Optimisation

## Slide 11: Misalignments
There are many facets of misalignments
The less we observe, the easier is the correction
Measurements in time sequences
aligned image
translation
rotation
scaling
shearing
isometric scaling

## Slide 12: Global transformations
Measurements in time sequences
Translation only
Translation
+ Rotation
Rigid transformation
Translation
+ Rotation
+ Isometric scaling
Geometric similar transformation
Translation
+ Rotation
+ scaling
[+shearing]
Affine transformation
fixed
moving

## Slide 13: Global transformations
These terms are variously used in registration software
Terminology

## Slide 14: Registration use cases
Use cases
Registration appears in many image pre-processing steps, such as
Motion correction
Image source: http://www.zmescience.com/medicine/gifs-biology-human-body/
Original
Image source: https://svi.nl/ChromaticAberrationCorrector
Chromatic aberration correction
Slice alignment
Image source: http://imagej.net/Register_Virtual_Stack_Slices
Stitching
Image source: Carine Stapel (Vastenhouw lab)
Multiview reconstruction
Image source: https://fiji.sc/ Multiview-Reconstruction

## Slide 15: Motion correction using StackReg
Select a frame, where the investigated object is as centred as possible.
Measurements in time sequences
Click menu Plugins > Registration > StackReg
Note: You need the update site “BIG-EPFL” activated in Fiji
Notes: White blood cells attacking a parasite @ 450x

## Slide 16: Quiz
If I would like to correct motion in this video, what kind of transformation should I use?
Translation
Rigid
Affine
Image source: http://www.zmescience.com/medicine/gifs-biology-human-body/

## Slide 17: Bleaching correction
Image > Adjust > Bleach Correction
Measurements in time sequences
Original
Simple ratio
Exponential fit
Histogram fit
Image source: Yu-Wen Hsieh, Tomancak lab, MPI CBG

## Slide 18: Measuring signal over time
Image > Stacks > Z-Axis profile
Measurements in time sequences

## Slide 19: Overview
Image correction
  Image registration
  Motion correction
  Bleaching correction
Visualisation
  Kymography
    How to build kymographs
    How to interpret kymographs
  Visualisation of time sequences in Imaris (Demo)
Tracking
  Introduction / Theory
  Single particle tracking
  Trackmate demo
  Exercise
Measurements in time sequences

## Slide 20: Kymography
Kymograph (“Wave writer”)
  documents water level over time
Kymograph images show signal along a line over time
Measurements in time sequences
Source: General physiology; an outline of the science of life (1899), London, Macmillan and co., limited

## Slide 21: Kymography
Measurements in time sequences
Dimension reduction
  2D+t 2D
To make further processing easier

## Slide 22: How to draw kymographs
Image > Stacks > Dynamic reslice
Measurements in time sequences
Do Image > Color > Split Channels and Z-Projection first
Keep in mind: You may move the yellow line after reslicing!

## Slide 23: How to draw kymographs
Alternatively:
Measurements in time sequences
pseudo y
z
pseudo y
t
Image > Duplicate
Image > Stacks > Dynamic reslice

## Slide 24: Kymograph: Interpretation
For speed estimation, we need information about
  distance and
Measurements in time sequences
time
space
  time
time
space
0.84 microns/second
1.18 microns/second
2.08 pixel/frame
  How fast are the chromosomes moving?

## Slide 25: Colour encoding time
Measurements in time sequences
Image > Hyperstack > Temporal-Color code
Image source: Imaris examle image

## Slide 26: Demo: Visualising time sequences in Imaris
Measurements in time sequences
DEMO

## Slide 27: Demo: Visualising time sequences in Imaris
Open images, from the Arena by drag and drop
Measurements in time sequences

## Slide 28: Demo: Visualising time sequences in Imaris
Edit > Show Display Adjustment
Measurements in time sequences

## Slide 29: Demo: Visualising time sequences in Imaris
Go to the Animation pane and add a Frame, marking the video start
Measurements in time sequences

## Slide 30: Demo: Visualising time sequences in Imaris
Go to a timepoint where a division is almost happening, add two (!) frames.
Measurements in time sequences

## Slide 31: Demo: Visualising time sequences in Imaris
Zoom in and add another frame.
Measurements in time sequences

## Slide 32: Demo: Visualising time sequences in Imaris
Continue in time until after the division and add another two (!) frames.
Measurements in time sequences

## Slide 33: Demo: Visualising time sequences in Imaris
Zoom out again (or Use the Reset view button) and add another frame.
Measurements in time sequences

## Slide 34: Demo: Visualising time sequences in Imaris
After all frames are added, click the Play button to view the video.
Click the Record button to export an AVI or MPG file.
Measurements in time sequences

## Slide 35
Coffee time!

## Slide 36: Overview
Image correction
  Image registration
  Motion correction
  Bleaching correction
Visualisation
  Kymography
    How to build kymographs
    How to interpret kymographs
  Visualisation of time sequences in Imaris (Demo)
Tracking
  Introduction / Theory
  Single particle tracking
  Trackmate demo
  Exercise
Measurements in time sequences

## Slide 37: Introduction
Tracking: ”following moving objects”
Very active research field
  algorithms
  applications
High computational effort (complexity)
  High performance computing
Goals
  Measure track properties (speed, velocity)
  Study spatio-temporal relationships
  Single particle tracking
  Building cell lineages during development
Measurements in time sequences
Source: Computer Vision Lab, ETH Zuerich
http://www.vision.ee.ethz.ch/datasets/
Source: Imaris (Bitplane) example image

## Slide 38: Introduction
Cell tracking in a nutshell…
Measurements in time sequences
With courtesy of Florian Jug, MPI CBG
Segmentation
t=1
Segmentation
t=2
matching
Segmentation
t=3
matching
Segmentation
matching
t-1
t
t+1
t-2
99% correct

## Slide 39: Cell tracking is an algorithmically difficult problem
Tracking needs many decisions…
Let’s assume we have:
  about 1000 objects
  500 time points (frames)
How many decisions are to be made?
  1000 + 499 * (1000+10002 ) = 499.500.000 (!!!)
Measurements in time sequences
With courtesy of Florian Jug, MPI CBG

## Slide 40: Cell tracking is an algorithmically difficult problem
Tracking errors propagate…
t → t + 1: 99% correct
Time points: 100
  P(‘correct lineage’) ≈ 0.9999 ≈ 37%
Time points: 500
  P(‘correct lineage’) ≈ 0.99499 ≈ 0.07%
Measurements in time sequences
With courtesy of Florian Jug, MPI CBG

## Slide 41: Cell tracking – main sources of errors
Erroneous segmentation
  )
Measurements in time sequences
With courtesy of Florian Jug, MPI CBG
2
1
How many objects do you see?

## Slide 42: Cell tracking – main sources of errors
Erroneous segmentation
  Missed objects (under-segmentation)
Measurements in time sequences
  Spurious objects (over-segmentation)
With courtesy of Florian Jug, MPI CBG

## Slide 43: Cell tracking – main sources of errors
Erroneous segmentation
  Missed objects (under-segmentation)
  Spurious objects (over-segmentation)
Erroneous Matching
Measurements in time sequences
t
t+1
t+2
With courtesy of Florian Jug, MPI CBG

## Slide 44: Terminology
Lineage tree (“graph”)
“Track”
“Edge”
“Node” / “Spot”
“Leaf”
“Root”
Measurements in time sequences
... just in case you talk to computer science guys

## Slide 45: Manual single particle tracking
Use the point tool to locate one particle in different (subsequent) time points.
Menu Edit > Options > Point Tool...
Measurements in time sequences

## Slide 46: Manual single particle tracking
... then just use other scientific software to do your analysis
Measurements in time sequences

## Slide 47: Manual single particle tracking
Use the multi-point tool to locate one particle in different (subsequent) time points.
Measurements in time sequences

## Slide 48: Exercise: speed measurements
Measure the speed of this one particular particle.
Measurements in time sequences
Do we have time for that?
30 min
no

## Slide 49: Exercise
Speed is distance travelled divided by time taken
Measurements in time sequences
Do we have time for that?
no

## Slide 50: Trackmate – your buddy for everyday tracking
Measurements in time sequences
DEMO

## Slide 51: Trackmate
Measurements in time sequences

## Slide 52: Trackmate: spot detection
Use and configure the LoG detector to get a good detection
Use the preview button!
Measurements in time sequences

## Slide 53: Trackmate: Spot detection
Measurements in time sequences

## Slide 54: Trackmate: tracking
The ”Simple LAP tracker” is fast and good but
The “LAP tracker” supports splitting and merging
Measurements in time sequences

## Slide 55: Trackmate: tracking
The ”Simple LAP tracker” is fast and good, but:
The “LAP tracker” supports splitting and merging
Measurements in time sequences

## Slide 56: Trackmate: filtering
Track filters allow for removing e.g. super short tracks
Measurements in time sequences

## Slide 57: Trackmate: lineage inspection
Use the TrackScheme to inspect lineages
Measurements in time sequences

## Slide 58: Trackmate: lineage inspection
Select tracks or single spots
Measurements in time sequences

## Slide 59: Trackmate: Add a spot
Press the A key (“Add”) to add a new spot at some position.
Press Q and E to increase or decrease the size of the spot.
Measurements in time sequences

## Slide 60: Trackmate: Add a linked spot
Select a spot by clicking on it
Activate linking mode by pressing SHIFT-L
Move forward in time and press A
Measurements in time sequences

## Slide 61: Trackmate: Link spots/tracks
Select spot A in timepoint t by clicking it
Go to timepoint t+1 and select spot B while holding SHIFT
Press L to link both spots
Measurements in time sequences

## Slide 62: Trackmate: Move spots
Hold the SPACE key while hovering over a spot. Move the mouse while holding the key.
Measurements in time sequences

## Slide 63: Remove tracks manually
Hover over a spot and press the D key (“Delete”)
Delete spots from the lineage view
Measurements in time sequences

## Slide 64: Trackmate: lineage curation
Cut a track where spots were wrongly connected.
Measurements in time sequences

## Slide 65: Trackmate: lineage curation
Wait until you see and then drag and drop to make a new connection.
Measurements in time sequences
DRAG
DROP

## Slide 66: Trackmate: Plotting
Plot measurements using Trackmate or export all measurements.
Measurements in time sequences

## Slide 67: Trackmate: Save tracks!
Don’t forget to save your tracks!
Save it after every important step – just in case ;-)
Measurements in time sequences

## Slide 68: Summary
Translation, rigid, affine registration
Measurements in time sequences
Draw and interpret Kymographs
Automatic tracking and manual curation

## Slide 69: Exercise
File > Open Samples > Tracks for Trackmate
Measure the length and mean velocity of the longest track
Explain the measurements
Measurements in time sequences