## Slide 1: Introduction to Image Analysis
Robert Haase, Benoit Lombardot
3D image segmentation and measurements
Contents
Segmentation in Fiji
Segmentation in Imaris
Measurements in 3D images

## Slide 2: Overview
Filtering in 3D
  Gaussian blur
Segmentation in Fiji
  HMaxima
  Watershed
  Volume manager
  Exercise
Segmentation in Imaris
  Demo
Measurements in Fiji
  Label analyser
  Constraint label maps
Exercise
3D image segmentation and measurements
0
11

## Slide 3: Introduction
Algorithms for 3D image segmentation are mostly the same like in 2D processing.
  Filters (Gaussian blur, image subtraction,...)
  Segmentation (thresholding, watershed, ...)
  Measurements (area → volume, circularity → sphericity)
However,
  configuration may be more complicated (Anisotropy),
  the 3D tools may have different names in Fiji menus,
  3D processing takes more time and
  consumes more memory.
3D image segmentation and measurements

## Slide 4: Filters: Gaussian blur in 2D
Process > Filters > Gaussian blur
3D image segmentation and measurements

## Slide 5: Filters: Gaussian blur in 2D
Process > Filters > Gaussian blur
3D image segmentation and measurements
x

## Slide 6: Filters: Gaussian blur in 3D
Process > Filters > Gaussian blur 3D
3D image segmentation and measurements

## Slide 7: Quiz
Process > Filters > Gaussian blur 3D
3D image segmentation and measurements
Does it work with physical units or with voxel units?
Physical units
Voxel units
Physical units
Voxel units

## Slide 8: Overview
Filtering in 3D
  Gaussian blur
Segmentation in Fiji
  HMaxima
  Watershed
  Volume manager
  Exercise
Segmentation in Imaris
  Demo
Measurements in Fiji
  Label analyser
  Constraint label maps
Exercise
3D image segmentation and measurements
0
11

## Slide 9: Segmentation in 3D
Similar algorithms like in 2D
  Thresholding,
  Local maxima detection,
  Watershed
Higher computational costs
  Memory
  Time
Inspection / reviewing is more complicated
  2D computer screen
3D image segmentation and measurements

## Slide 10: Detection versus Segmentation
3D image segmentation and measurements
Original image
Channel for nuclei detection
Points marking nuclei
Nuclei label map
Channel for cell segmentation
Cell label map
ROIs / outlines
Resulting segmentation on original image
Image source: Akanksha Jain, Tomancak Lab, MPI CBG

## Slide 11: HMaxima detection
If local maxima (bright/dark spots in the image) represent objects of interest/to count, it may be worthwhile to detect local maxima.
If these maxima raise from the background by a certain amount, HMaxima may be the algorithm to go.
Afterwards: Use watershed to segment the objects
3D image segmentation and measurements
h4
h3
h1
h2
h1’
H-maxima principle

## Slide 12: HMaxima detection + Watershed segmentation
3D image segmentation and measurements
DEMO

## Slide 13: HMaxima based detection
Analyse > Plot Profile
3D image segmentation and measurements
Image source: Elena Gromberg, Tanaka Group, CRTD

## Slide 14: HMaxima based detection
Process > Filters > Gaussian Blur 3D…
3D image segmentation and measurements
Image source: Elena Gromberg, Tanaka Group, CRTD

## Slide 15: HMaxima based detection
SCF > Labeling> HMaxima local maximum detection…
3D image segmentation and measurements
Image source: Elena Gromberg, Tanaka Group, CRTD
tmin
hmin

## Slide 16: Postprocessing using watershed
SCF > Labeling > Watershed…
3D image segmentation and measurements
Hint: If it’s not displayed correctly, just open the Image > Adjust > Brightness/Contrast dialog

## Slide 17: Volume manager
Fiji menu: SCF > Segmentation > Volume manager
Select the label map
Volume manager menu: File > Import > Import labelmap
Switch back to original image
3D image segmentation and measurements

## Slide 18: Reslicing resulting label maps
Check the resulting label maps properly – the Gaussian and HMaxima parameters may be improvable!
Use 3D visualisation if needed
3D image segmentation and measurements

## Slide 19: Exercise
Open “test_12h_0.1x0.1x0.25.tif”
Try to segment the given data set properly.
How many cells can you differentiate in the green channel?
How did you configure HMaxima to get this number?
3D image segmentation and measurements
16?

## Slide 20: Demo: 3D Segmentation in Imaris
3D image segmentation and measurements
Demo

## Slide 21: Demo: 3D Segmentation in Imaris
Open a data set from the Arena or by drag&drop
3D image segmentation and measurements

## Slide 22: Demo: 3D Segmentation in Imaris
Create a new Surface and follow the instructions in the bottom left corner
Select the channel where the objects are
Switch to view and measure the diameter of one object.
Enter that value as seed points diameter
3D image segmentation and measurements

## Slide 23: Demo: 3D Segmentation in Imaris
Filter the detected spots by quality
3D image segmentation and measurements

## Slide 24: Demo: 3D Segmentation in Imaris
Filter surfaces
3D image segmentation and measurements

## Slide 25: Demo: 3D Segmentation in Imaris
Switch to statistcs view and inspect the individual objects
3D image segmentation and measurements

## Slide 26: Overview
Filtering in 3D
  Gaussian blur
Segmentation in Fiji
  HMaxima
  Watershed
  Volume manager
  Exercise
Segmentation in Imaris
  Demo
Measurements in Fiji
  Label analyser
  Constraint label maps
Exercise
3D image segmentation and measurements
0
11

## Slide 27: Measurements in 3D
Obviously, some measurements in 2D and 3D differ:
  Area → Volume,
  Circularity → Sphericity,
  Perimeter length → Surface area
Many others are in principle identical
  Mean average signal...
  Minimum/maximum signal,
  ...
Again, tools may be called and work differently:
  Particle analyser → Label analyser
3D image segmentation and measurements

## Slide 28: Label analyser
SCF > Labeling > Label Analyser (2D, 3D)
3D image segmentation and measurements

## Slide 29: Label analyser
SCF > Labeling > Label Analyser (2D, 3D)
3D image segmentation and measurements

## Slide 30: Constraint label map
Typical pipeline extended by:
Constraint or filter resulting object detection/segmentation
  By measuring object properties
3D image segmentation and measurements
Detect
Segment
Measure
Constraint
Measure
Find maxima
Watershed
Region growing
Thresholding
Connected components labeling
Particle analyser
Label analyser

## Slide 31: Constraint label map
Menu SCF > Labeling > Constraint label map
Constraint minimum volume
3D image segmentation and measurements

## Slide 32: Constraint label map
Menu SCF > Labeling > Constraint label map
Constraint minimum and maximum volume
3D image segmentation and measurements

## Slide 33: Constraint label map
Constraint for number of neighbours closer than 25 pixels using the label analyser
3D image segmentation and measurements
0
11

## Slide 34: Constraint label map
Constraint for number of neighbours closer than 25 pixels using the label analyser
3D image segmentation and measurements

## Slide 35: Summary
3D image segmentation and measurements
Apply 3D filters
Detect and segment objects in 3D
Select / constraint objects according to measurements in 3D

## Slide 36: Overview
Filtering in 3D
  Gaussian blur
Segmentation in Fiji
  HMaxima
  Watershed
  Volume manager
  Exercise
Segmentation in Imaris
  Demo
Measurements in Fiji
  Label analyser
  Constraint label maps
Exercise
3D image segmentation and measurements
0
11

## Slide 37: Exercise
Unpack the file HisYFP-SPIM.zip
It contains SPIM images of a Drosophila embryo.
Question:
  How many nuclei does the embryo consist of?
Exercise: Count nuclei in 3D SPIM data
Image source: https://imagej.net/Multiview-Reconstruction

## Slide 38: Exercise: hints
Use multiview-reconstruction to fuse the SPIM measurements in one 3D volume
Use background subtraction to make the nuclei better visible
Use HMaxima and seeded watershed to detect nuclei
Constraint the resulting label map to differentiate actual nuclei and false-positive detections.
Exercise: Count nuclei in 3D SPIM data

## Slide 39: Hint: Background subtraction
Process > Subtract background
Exercise: Count nuclei in 3D SPIM data

## Slide 40: Hint: HMaxima
SCF > Labeling > HMaxima local maximum detection
Exercise: Count nuclei in 3D SPIM data

## Slide 41: Hint: Watershed
SCF > Labeling > Watershed with seed points
Exercise: Count nuclei in 3D SPIM data

## Slide 42: Hint: Measure
SCF > Labeling > Label Analyser
What’s a good measure to differentiate cells from false positive detections?
Exercise: Count nuclei in 3D SPIM data

## Slide 43: Hint: Constraint labels
SCF > Labeling > Constraint labels in a label map
Constraint for measured label properties
Exercise: Count nuclei in 3D SPIM data

## Slide 44: Hint: 3D Viewer
Visualise detection/segmentation
Exercise: Count nuclei in 3D SPIM data

## Slide 45: Hint: ClearVolume
Visualise measurements
Exercise: Count nuclei in 3D SPIM data
0
13